## Slide 1
AI SKIN DISEASE
DETECTION
An end-to-end prototype for image capture, non-skin rejection, skin-lesion screening, and report generation
Camera → AI → Report
Project presentation | Hardware + Python + TensorFlow Lite
Educational prototype — not a medical diagnostic device
Notes: Presenter note: Use this slide to explain the project sequence.
[Sources]
Project source: https://github.com/Vishal123-tech/AI-Skin-Disease-Detection-System

## Slide 2
CONTENTS
The presentation follows the complete build journey
02
01 Abstract
02 Problem definition
03 Literature review
04 Introduction
05 Proposed block diagram
06 Circuit / algorithm / flowchart
07 Software used
08 Hardware used
09 Methodology / mathematical analysis
10 Expected results
11 Conclusion
12 Plan
13 End-to-end demonstration
14 Final status
Central idea: capture a good image, reject non-skin inputs, classify cautiously, and generate an explainable report.
Notes: Presenter note: Use this slide to explain the project sequence.
[Sources]
Source: User-provided contents reference image.
Project source: https://github.com/Vishal123-tech/AI-Skin-Disease-Detection-System

## Slide 3
ABSTRACT
The system turns a camera image into a cautious screening report
03
This project is an educational prototype that combines a camera, a Python web service, and an image classifier. The system captures a skin image, evaluates image quality, checks whether the input is likely to contain skin, classifies supported lesion categories, and generates a downloadable PDF report.
Input
Camera or uploaded image
Intelligence
Quality checks + model inference
Output
Prediction, confidence, PDF report
The goal is not to replace a clinician. The goal is to demonstrate a complete, testable AI-enabled hardware workflow.
Notes: Presenter note: Use this slide to explain the project sequence.
[Sources]
Project source: https://github.com/Vishal123-tech/AI-Skin-Disease-Detection-System

## Slide 4
PROBLEM DEFINITION
A classifier can be confidently wrong when the input is not skin
04
Random input
Tables, fans, notes, rooms, and animals may be forced into the closest disease class.
Model bias
A dominant training class can appear repeatedly even when the image does not match it.
Scope gap
The current local model supports a limited label set; it cannot know conditions absent from training.
Design principle
Reject clearly invalid inputs before disease classification, and report uncertainty instead of inventing certainty.
Notes: Presenter note: Use this slide to explain the project sequence.
[Sources]
Project behavior observed during local testing and user-provided screenshots.
Project source: https://github.com/Vishal123-tech/AI-Skin-Disease-Detection-System

## Slide 5
LITERATURE REVIEW
The design combines established building blocks
05
Medical image datasets
ISIC / HAM-style lesion images provide labeled examples for research classifiers.
Transfer learning
MobileNetV2 reduces training cost by starting from learned visual features.
Edge inference
TensorFlow Lite enables a smaller model to run on constrained devices.
Human-centered screening
Quality warnings, uncertainty, and a clear disclaimer reduce over-interpretation.
The contribution of this project is integration: camera capture, validation, inference, API response, and reporting in one workflow.
Notes: Presenter note: Use this slide to explain the project sequence.
[Sources]
ISIC datasets: https://challenge.isic-archive.com/data/
TensorFlow Lite: https://www.tensorflow.org/lite
MobileNetV2: https://arxiv.org/abs/1801.04381

## Slide 6
INTRODUCTION
The project is a pipeline, not just a prediction model
06
→
→
→
→
Capture
Validate
Reject
Classify
Report
Capture
Use a Raspberry Pi Camera Module or browser upload.
Validate
Check blur, brightness, resolution, and file readability.
Reject
Use skin-color, entropy, and document-like safeguards.
Classify
Run the supported local model and expose top predictions.
Report
Return JSON and generate a PDF summary.
Notes: Presenter note: Use this slide to explain the project sequence.
[Sources]
Project source: https://github.com/Vishal123-tech/AI-Skin-Disease-Detection-System

## Slide 7
PROPOSED BLOCK DIAGRAM
The hardware, web service, model, and report form one closed loop
07
Camera
(Raspberry Pi)
Flask API
/api/predict
Image quality
+ skin gate
TFLite disease
classifier
JSON + PDF
report
→
→
→
→
Control loop
The user receives a result, improves the image if needed, and can capture again without changing the model.
Notes: Presenter note: Use this slide to explain the project sequence.
[Sources]
Project source: https://github.com/Vishal123-tech/AI-Skin-Disease-Detection-System

## Slide 8
ALGORITHM / FLOWCHART
Every image follows the same decision sequence
08
1
Receive image
2
Read + resize
3
Quality check
4
Skin / non-skin gate
5
Model inference
6
Report result
Decision logic
if image_invalid:
request_clearer_photo()
elif non_skin_detected:
reject_input()
elif confidence_low:
return_uncertain()
else:
return_prediction_and_report()
Notes: Presenter note: Use this slide to explain the project sequence.
[Sources]
Project source: https://github.com/Vishal123-tech/AI-Skin-Disease-Detection-System

## Slide 9
SOFTWARE USED
The software stack keeps capture, inference, and reporting separate
09
Application
Python
Flask API
Gradio interface
AI / vision
TensorFlow Lite
OpenCV
Pillow
Output
ReportLab PDF
JSON API
Render deployment
Development loop
Build locally → test with known inputs → validate the API → deploy only after review
Optional training tools: TensorFlow / PyTorch transfer learning, with the final runtime exported as a lightweight TFLite model.
Notes: Presenter note: Use this slide to explain the project sequence.
[Sources]
Flask: https://flask.palletsprojects.com/
TensorFlow Lite: https://www.tensorflow.org/lite
ReportLab: https://www.reportlab.com/
Project source: https://github.com/Vishal123-tech/AI-Skin-Disease-Detection-System

## Slide 10
HARDWARE USED
The Raspberry Pi can run headlessly with the phone as the display
10
Raspberry Pi
Zero 2 W, Pi 4, or Pi 5
Camera Module
Captures the skin image
MicroSD card
OS, Python environment, model
Power + Wi-Fi
Stable operation and browser access
No Raspberry Pi display is required: open http://PI_IP_ADDRESS:5000 from a phone or laptop on the same network.
Notes: Presenter note: Use this slide to explain the project sequence.
[Sources]
Raspberry Pi Camera software: https://www.raspberrypi.com/documentation/computers/camera_software.html
Project source: https://github.com/Vishal123-tech/AI-Skin-Disease-Detection-System

## Slide 11
METHODOLOGY / MATHEMATICAL ANALYSIS
Methodology makes the model measurable and deployable
11
Training
• Organize images by label
• Split train / validation / test
• Resize to the model input
• Apply augmentation only to training data
• Export the trained network to TFLite
Prediction
p = softmax(z)
confidence = max(p)
entropy = −Σ pᵢ log₂(pᵢ)
accept only when quality
and confidence are adequate
Key evaluation measures
Accuracy is not enough: measure non-skin false positives, recall, confusion, and performance across lighting and skin tones.
Notes: Presenter note: Use this slide to explain the project sequence.
[Sources]
Softmax and entropy are standard statistical tools; implementation is in the project predictor.py.
Project source: https://github.com/Vishal123-tech/AI-Skin-Disease-Detection-System

## Slide 12
EXPECTED RESULTS
Success means fewer false positives and clearer user feedback
12
Reject
Documents, handwritten pages, tables, fans, rooms, animals, and random objects.
Recognize
Supported skin-lesion classes and normal skin only within the trained scope.
Explain
Show confidence, quality metrics, notes, and a PDF report.
Deploy
Run from a browser, Raspberry Pi camera, or API client.
These are acceptance goals, not claimed medical accuracy. Final performance must be measured on a held-out dataset.
Notes: Presenter note: Use this slide to explain the project sequence.
[Sources]
Expected results are project acceptance goals, not measured claims.
Project source: https://github.com/Vishal123-tech/AI-Skin-Disease-Detection-System

## Slide 13
CONCLUSION
The value is in the complete system
A camera becomes useful when the surrounding workflow handles quality, rejects invalid inputs, reports uncertainty, and leaves a traceable result.
Capture • Validate • Reject • Classify • Report
Educational screening prototype — always confirm concerns with a qualified healthcare professional.
Notes: Presenter note: Use this slide to explain the project sequence.
[Sources]
Project source: https://github.com/Vishal123-tech/AI-Skin-Disease-Detection-System

## Slide 14
PLAN
The remaining plan is to train, integrate, validate, and then release
14
1
Dataset
Finalize skin + non-skin gate data
→
2
Training
Train the small TFLite gate in Colab
→
3
Integration
Run gate before disease model
→
4
Validation
Test random images and skin images
→
5
Release
Push the verified model to Render
Next action: train the gate model in Google Colab and return skin_gate.tflite for local testing.
Notes: Presenter note: Use this slide to explain the project sequence.
[Sources]
Project source: https://github.com/Vishal123-tech/AI-Skin-Disease-Detection-System

## Slide 15
END-TO-END DEMONSTRATION
One complete run looks like this
15
01
Power on
Pi boots and camera is ready
02
Capture
Camera saves a JPEG
03
Upload
POST /api/predict receives image
04
Decide
Quality + skin gate + classifier
05
Deliver
Browser result + PDF report
POST /api/predict
Notes: Presenter note: Use this slide to explain the project sequence.
[Sources]
Project source: https://github.com/Vishal123-tech/AI-Skin-Disease-Detection-System

## Slide 16
FINAL STATUS
Current status: the prototype is working and ready for the gate-model step
16
Completed
Web app
TFLite model
PDF reports
Render deployment
Prepared
Skin dataset
COCO non-skin dataset
Raspberry Pi capture flow
Next
Train gate model
Integrate locally
Validate, then release
Thank you
Questions and demonstration
GitHub: github.com/Vishal123-tech/AI-Skin-Disease-Detection-System
Notes: Presenter note: Use this slide to explain the project sequence.
[Sources]
Project source: https://github.com/Vishal123-tech/AI-Skin-Disease-Detection-System